## Slide 1: Classification of Electroencephalogram (EEG) data with Neural Nets Supervisor : Prof.Dr. ERTUĞRUL TAÇGIN – Arş. Gör. EMRE ARI
Özgürazad Çelik - 524618020
ME7000 Seminar

## Slide 2: Contents
Structure of Human Brain
Electroencephalography(EEG)
Types of Brainwaves
Brain-Computer Interface (BCI)
Components of a BCI system
ANN
CNN
EEG data classification with ANN and CNN
Conclusion
References

## Slide 3: Neurons

## Slide 4: Action Potential

## Slide 5: Anatomy of the Brain

## Slide 6: What is an EEG?
An EEG test evaluates the electrical activity of the brain. EEG scans are performed by placing EEG sensors – small metal discs also called EEG electrodes – on our scalp. These electrodes pick up and record the electrical activity in our brain. The collected EEG signals are amplified, digitized, and then sent to a computer or mobile device for storage and data processing.
Analyzing EEG data is an exceptional way to study cognitive processes: It can help doctors establish a medical diagnosis, researchers understand the brain processes that underlie human behavior, and individuals to improve their productivity and wellness.

## Slide 8: Types of Brainwaves that EEG Measures
The electrodes of an EEG device capture electrical activity expressed in various EEG frequencies. Using an algorithm called a Fast Fourier Transform (FFT), these raw EEG signals can be identified as distinct waves with different frequencies. Frequency, which refers to the speed of the electrical oscillations, is measured in cycles per second—one Hertz (Hz) is equal to one cycle per second. Brainwaves are categorized by frequency into four main types: Beta, Alpha, Theta and Delta.

## Slide 9: Delta Waves (δ, 0.5-4Hz)
Delta activity is predominantly found in infants. Delta waves are associated with deep stages of sleep in older subjects.
Delta waves are characterized by low-frequency (about 3 Hz), high amplitude waves. Delta rhythms can be present during wakefulness—they are responsive to eye-opening and may be enhanced by hyperventilation as well. When measured by an EEG device, these are often referred to as EEG delta waves.

## Slide 10: Theta Waves (θ, 4-8Hz)
Brain activity within a frequency range comprised between 4 and 7 Hz is referred to as Theta activity. Theta rhythm detected in EEG measurement is often found in young adults, particularly over the temporal regions and during hyperventilation. In older individuals, theta activity with an amplitude greater than about 30 millivolts (mV) is seen less commonly.

## Slide 11: Alpha Waves (α, 8-13Hz)
Alpha waves are often associated with a relaxed, calm and lucid state of mind. Alpha waves can be found in the occipital and posterior regions of the brain. Alpha waves can be induced by closing one’s eyes and relaxing, and they are rarely present during intense cognitive processes like thinking, mental calculus and problem-solving. In most adults, alpha waves range in frequency from 9 to 11 Hz. When measured by an EEG device, these are often referred to as EEG alpha waves.

## Slide 12: Beta Waves (β, 13-30Hz)
Beta waves are most closely associated with being conscious or in an awake, attentive and alert state. Low-amplitude beta waves are associated with active concentration, or with a busy or anxious state of mind. Beta waves are also associated with motor decisions (suppression of movement and sensory feedback of motion). When measured by an EEG device, the signals are often referred to as EEG beta waves.

## Slide 13: Gamma Waves (γ, >30Hz):
The occurrence of the gamma waves is rare and they have been used to detect specific diseases. The region of these waves cover frontocentral area on the brain.

## Slide 14: Waveforms

## Slide 15: Brain-Computer Interface (BCI)
Devices that enable its users to interact with computers by mean of brain-activity only, this activity being generally measured by ElectroEncephaloGraphy (EEG).

## Slide 16: Types of BCI
Brain computer interfaces can be classified in three main groups:

## Slide 17: Electrical signals from brain activity are detected by recording electrodes located on the scalp, on the cortical surface, or within the brain. The brain signals are amplified and digitized. Pertinent signal characteristics are extracted and then translated into commands that control an output device, such as a spelling program, a motorized wheelchair, or a prosthetic limb. Feedback from the device enables the user to modify the brain signals in order to maintain effective device performance.
Components of a BCI system

## Slide 18: Signal acquisition
Signal acquisition is the measurement of brain signals using a particular sensor modality (eg, scalp or intracranial electrodes for electrophysiologic activity, fMRI for metabolic activity). The signals are amplified to levels suitable for electronic processing (and they may also be subjected to filtering to remove electrical noise or other undesirable signal characteristics, such as 60-Hz power line interference). The signals are then digitized and transmitted to a computer.

## Slide 19: Extraction and Selection

## Slide 20: Feature Extractıon
Feature extraction works around the idea of extracting useful features that clearly identify objects in an image.
It involves reducing the number of resources required to describe a large dataset, it is dimension reduction.

## Slide 21: Feature Extractıon
Why we use Feature Extraction
Performing analysis with a large number of variables often requires large amounts of memory and computational power
Too many features can increase the complexity of our model, leading to an overfit.
Feature extraction; It defines the data with sufficient accuracy and uses different types of filters to transform it with the image to overcome these problems.

## Slide 22: Feature Translation
The resulting signal features are then passed to the feature translation algorithm, which converts the features into the appropriate commands for the output device (ie, commands that accomplish the user's intent). For example, a power decrease in a given frequency band could be translated into an upward displacement of a computer cursor, or a P300 potential could be translated into selection of the letter that evoked it. The translation algorithm should be dynamic to accommodate and adapt to spontaneous or learned changes in the signal features and to ensure that the user's possible range of feature values covers the full range of device control.

## Slide 23: Device Output
The commands from the feature translation algorithm operate the external device, providing functions such as letter selection, cursor control, robotic arm operation, and so forth. The device operation provides feedback to the user, thus closing the control loop.

## Slide 24: BCI Eletrodes

## Slide 25: Artificial Neural Networks
Neural networks are information processing systems with interconnected neurons. Using certain algorithms they can recognize, cluster, and classify hidden patterns and correlations in raw data and continually learn and improve – over time.

## Slide 26: Forward Propagation
Our input data is given to artificial neural networks. The weight values in our artificial neural network in our neurons are given randomly.
The data in the input neuron is sent to the next neuron with the weight values.
Each neuron multiplies and sums the values and weights of the neurons connected to it. This result is being given as input into the activation function.

## Slide 27: Back Propagation
The prediction results from the neurons in the output layer are compared with the real value and the error is calculated. Using these error values and the weight values of the previous layer, the error of the previous layer is calculated.
Gradients are calculated using the calculated error values. Weight values are recalculated using these gradients.

## Slide 29: What ıs Actıvatıon Functıon?
The activation function, in its simplest form, is the function that decides how a linear function calculated using the inputs of a neuron will exit the neuron.
It is used to distort the linearity and determines how the linearity will be distorted.
A classical neuron does not have an activation function unless given manually and performs a linear computation.

## Slide 30: Convolutıonal Neural Network CNNs

## Slide 31: Convolutional Neural Network

## Slide 32: CNN and Layers
CNN layers;
Convolutional Layer
Pooling
(Downsampling Layer)
Stride
Padding
Flattening Layer
Fully-Connected Layer

## Slide 33: Input Layer
The input layer in CNN should contain the image data. Image data is represented by a multidimensional matrix and reshaped into a single vector within the input layer.
For example, you have a 28x28 image. This image is converted into a 784x1 vector as 28x28=784 before processing.

## Slide 34: Stride
We express the number of rows and columns covered per shift as stride.
The number of stride does not have to be one. Sometimes, either for computational efficiency or because we want to downsample, we move our window multiple items at once, bypassing intermediate positions.

## Slide 35: Padding
One problem with applying convolutional layers is that we tend to lose pixels around our image.
Especially when we apply many sequential convolution layers, pixel losses can be experienced intensely.
A simple solution to this problem is to add extra padding pixels around the border of our input image, thus increasing the effective size of the image.

## Slide 36: Convolution Layer
The convolution layer (CONV) uses filters that perform convolution operations while scanning the input layer by size.
The resulting output is called the feature map or activation map.

## Slide 37: Pooling Layer
It is used to reduce the size of feature maps. Thus, it reduces the number of parameters to be learned in the network and the amount of calculations made.

## Slide 38: Flattenıng Layer
Once the Feature Map is obtained, the next step is to flatten it.
Flattening involves converting the entire pooled feature map matrix into a single column and feeding the neural network for further processing

## Slide 39: Fully Connected Layer
A fully connected layer (FC) is a layer where all inputs in one layer are connected to each unit of the next layer. It is a standard neural network layer.
Fully connected layers can be used to optimize goals such as class scores.
The biggest advantage of fully connected layers is; They are structure independent. No special assumptions to be made about the input

## Slide 40: What is a Pre-Trained Model
A pre-trained model is a registered network that has been previously trained on a large dataset, typically a large-scale image classification task. You either use the pre-trained model as is, or you use transfer learning to customize this model for a specific task.
xception
Inception V3
ResNet50
VGG16
VGG19
MobileNet

## Slide 41: Convolutional Neural Network and BCI
One advantage of using deep learning technique is that it requires minimal pre-processing since optimal settings are learned automatically. Regarding CNNs, feature extraction and classification are integrated into a single structure and optimized automatically. Moreover, fNIRS time series data of human subjects were input to the CNN. As the convolution is performed in the sliding show manner, the feature extraction process of CNN retains the temporal information of the time series data obtained by fNIRS.

## Slide 42: EEG data classification with ANN and CNN
In this study, a total of 16 EEG data from 8 subjects were classified with ANN and CNN.
There are 2 classes in the study.
It contains the measurement data for the movements that the first class subjects made as defined.
The other class contains data measuring undefined movements.

## Slide 43: EEG data classification with CNN

## Slide 44: Loading Libraries
import pandas as pd
import numpy as np
import matplotlib.pyplot as plt
import scipy.stats as scs
import re
from numpy import genfromtxt
import tensorflow as tf
import keras
from sklearn.model_selection import KFold
from keras.utils import to_categorical
from keras.layers import LSTM, Conv1D, MaxPooling1D, Flatten, Embedding, GlobalAveragePooling1D
from tensorflow.keras.constraints import max_norm
from keras.models import Sequential
from keras.layers import Dense, Flatten, Conv2D, Dropout, BatchNormalization, MaxPooling2D, Activation, SpatialDropout1D, GlobalMaxPooling1D, TimeDistributed
from keras.losses import sparse_categorical_crossentropy
from keras.optimizers import Adam

## Slide 45: Data Import
data1 = data1.to_numpy()
data2 = data2.to_numpy()
data3 = data3.to_numpy()
data4 = data4.to_numpy()
data5 = data5.to_numpy()
data6 = data6.to_numpy()
data7 = data7.to_numpy()
data8 = data8.to_numpy()
data9 = data9.to_numpy()
data10 = data10.to_numpy()
data11 = data11.to_numpy()
data12 = data12.to_numpy()
data13 = data13.to_numpy()
data14 = data14.to_numpy()
data15 = data15.to_numpy()
data16 = data16.to_numpy()
data1 = pd.read_csv("eeg/ML101_KS.csv").T
data2= pd.read_csv("eeg/ML101_US.csv").T
data3= pd.read_csv("eeg/ML102_KS.csv").T
data4= pd.read_csv("eeg/ML102_US.csv").T
data5= pd.read_csv("eeg/ML103_KS.csv").T
data6= pd.read_csv("eeg/ML103_US.csv").T
data7= pd.read_csv("eeg/ML104_KS.csv").T
data8= pd.read_csv("eeg/ML104_US.csv").T
data9= pd.read_csv("eeg/ML105_KS.csv").T
data10= pd.read_csv("eeg/ML105_US.csv").T
data11= pd.read_csv("eeg/ML106_KS.csv").T
data12= pd.read_csv("eeg/ML106_US.csv").T
data13= pd.read_csv("eeg/ML107_KS.csv").T
data14= pd.read_csv("eeg/ML107_US.csv").T
data15= pd.read_csv("eeg/ML108_KS.csv").T
data16= pd.read_csv("eeg/ML108_US.csv").T
labels = [1,0,1,0,1,0,1,0,1,0,1,0,1,0,1,0]

## Slide 46: Organizing data
data1 = np.expand_dims(data1, axis=0)
data2 = np.expand_dims(data2, axis=0)
data3 = np.expand_dims(data3, axis=0)
data4 = np.expand_dims(data4, axis=0)
data5 = np.expand_dims(data5, axis=0)
data6 = np.expand_dims(data6, axis=0)
data7 = np.expand_dims(data7, axis=0)
data8 = np.expand_dims(data8, axis=0)
data9 = np.expand_dims(data9, axis=0)
data10 = np.expand_dims(data10, axis=0)
data11 = np.expand_dims(data11, axis=0)
data12 = np.expand_dims(data12, axis=0)
data13 = np.expand_dims(data13, axis=0)
data14 = np.expand_dims(data14, axis=0)
data15 = np.expand_dims(data15, axis=0)
data16 = np.expand_dims(data16, axis=0)
data1 = data1[:,:13000,:]
data2 = data2[:,:13000,:]
data3 = data3[:,:13000,:]
data4 = data4[:,:13000,:]
data5 = data5[:,:13000,:]
data6 = data6[:,:13000,:]
data7 = data7[:,:13000,:]
data8 = data8[:,:13000,:]
data9 = data9[:,:13000,:]
data10 = data10[:,:13000,:]
data11 = data11[:,:13000,:]
data12 = data12[:,:13000,:]
data13 = data13[:,:13000,:]
data14 = data14[:,:13000,:]
data15 = data15[:,:13000,:]
data16 = data16[:,:13000,:]
data_all = np.concatenate((data1, data2, data3, data4, data5, data6, data7, data8, data9, data10, data11, data12, data13, data14, data15, data16), axis = 0)

## Slide 47: ANN
data1.shape
(1, 13000, 13)
labels = np.array(labels)
model = Sequential()
model.add(tf.keras.layers.Flatten())
model.add(tf.keras.layers.Dense(1000, activation = "relu"))
model.add(tf.keras.layers.Dense(500, activation = "relu"))
model.add(tf.keras.layers.Dense(100, activation = "relu"))
model.add(tf.keras.layers.Dense(50, activation = "relu"))
model.add(tf.keras.layers.Dense(10, activation = "relu"))
model.add(tf.keras.layers.Dense(2, activation = "softmax"))
optimizer = keras.optimizers.Adam(learning_rate = 1e-4)
model.compile(optimizer = optimizer, loss = "sparse_categorical_crossentropy", metrics = ["accuracy"])
model_history = model.fit(data_all, labels, batch_size = 16, validation_split = 0.2, epochs = 50)

## Slide 48: ANN Summary

## Slide 49: ANN Results

## Slide 50: CNN
from sklearn.model_selection import train_test_split
x_train, x_test, y_train, y_test = train_test_split(data_all, labels, test_size = 0.2)
model_cnn = Sequential()
model_cnn.add(tf.keras.layers.Conv1D(filters = 16, input_shape = (13000, 13), kernel_size = 20, activation = "relu"))
model_cnn.add(tf.keras.layers.BatchNormalization())
model_cnn.add(tf.keras.layers.MaxPooling1D(pool_size = 2))
model_cnn.add(tf.keras.layers.Dropout(0.2))
model_cnn.add(tf.keras.layers.Conv1D(filters = 32, kernel_size = 20, activation = "relu"))
model_cnn.add(tf.keras.layers.BatchNormalization())
model_cnn.add(tf.keras.layers.MaxPooling1D(pool_size = 2))
model_cnn.add(tf.keras.layers.Dropout(0.2))
model_cnn.add(tf.keras.layers.Conv1D(filters = 64, kernel_size = 20, activation = "relu"))
model_cnn.add(tf.keras.layers.BatchNormalization())
model_cnn.add(tf.keras.layers.Dropout(0.2))
model_cnn.add(tf.keras.layers.Flatten())
model_cnn.add(tf.keras.layers.Dense(10, activation = "relu"))
model_cnn.add(tf.keras.layers.BatchNormalization())
model_cnn.add(tf.keras.layers.Dropout(0.2))
model_cnn.add(tf.keras.layers.Dense(2, activation = "softmax"))
callback = tf.keras.callbacks.EarlyStopping(monitor = "val_loss", patience = 20, restore_best_weights = True)
optimizer = keras.optimizers.Adam(learning_rate = 1e-4)
model_cnn.compile(optimizer = optimizer, loss = "sparse_categorical_crossentropy", metrics = ["accuracy"])
model_cnn_history = model_cnn.fit(x_train, y_train, batch_size = 4, validation_data = (x_test, y_test), epochs = 100, callbacks = [callback])

## Slide 51: CNN Results

## Slide 52: CNN Summary

## Slide 53: ANN VS CNN

## Slide 54: Conclusion
Traditional Machine learning algorithms require many different tools for feature extraction and feature selection. These methods, which are used to lighten the processing load when computers have weak processing power, may cause the signal to lose the information it contains. The aim is to classify data with the least information loss. Therefore, ANN and CNN, which can work without the need for signal processing, are efficient tools for this study. In studies where the data set is very large, CNN structure is expected to classify much better than ANN. Normally ANN is expected to give higher accuracy on small dataset. However, ANN parameters were not changed much in this study. Therefore, the accuracy value of CNN was found to be higher than ANN.

## Slide 55: References
The Introductory Guide to EEG (Electroencephalography) – EMOTIV
A brain–computer interface using electrocorticographic signals in humans - Eric C Leuthardt, Gerwin Schalk, Jonathan R Wolpaw,Jeffrey G Ojemann and Daniel W Moran5
Brain-Computer Interfaces in Medicine - Jerry J. Shih, Dean J. Krusienski and Jonathan R. Wolpawc
Brain–computer interfaces for communication and control - Jonathan R Wolpaw, Niels Birbaumer, Dennis J McFarlanda, Gert Pfurtschellere, Theresa M Vaughana
A Beginner’s Guide to Brain-Computer Interface and Convolutional Neural Networks | by Alexandre Gonfalonieri | Towards Data Science
World’s fastest brain-computer interface: Combining EEG2Code with deep learning - Sebastian Nagel, Martin Spüler
Learning Representations from EEG with Deep Recurrent-Convolutional Neural Networks - Pouya Bashivan, Irina Rish, M. Yeasin, Noel Codella
EDF Tools – Eurochamp Data Center
Transfer Learning Using AlexNet - MATLAB & Simulink (mathworks.com)
A novel approach of decoding EEG four-class motor imagery tasks via scout ESI and CNN - Yimin Hou, Lu Zhou, Shuyue Jia and Xiangmin Lun
A Deep Learning MI-EEG Classication Model for BCIs - Dose, Hauke; Møller, Jakob Skadkær; Puthusserypady, Sadasivan; Iversen, Helle K.
EEGNet: A Compact Convolutional Network for EEG-based Brain-Computer Interfaces - Vernon J. Lawhern, Amelia J. Solon, Nicholas R. Waytowich, Stephen M. Gordon, Chou P. Hung, Brent J. Lance
Temple University EEG Corpus - Downloads (piconepress.com)
A Simplified CNN Classification Method for MI-EEG via the Electrode Pairs Signals - Xiangmin Lun, Zhenglin Yu, Tao Chen, Fang Wang and Yimin Hou
EEG Motor Movement/Imagery Dataset v1.0.0 (physionet.org)
5. Preprocess data - EEGLAB Wiki

## Slide 56: Thank you for listening!